## Slide 1: Disk and New Storage Devices
毛 波
厦门大学 信息学院

## Slide 2: The first HDD (1956)
IBM 305 RAMAC
4 MB
50x24” disks
1200 rpm
100 ms access
35k$/y rent
Included computer & accounting software (tubes not transistors)

## Slide 3: 10 years later
1.6 meters

## Slide 4: Transportation of HDD

## Slide 5
1 inch disk drive!
2000 IBM MicroDrive:
  1.7” x 1.4” x 0.2”
  1 GB, 3600 RPM, 5 MB/s, 15 ms seek
  Digital camera, PalmPC?
2006 MicroDrive
  8 GB, 50 MB/s!

## Slide 6: The internal look of HDD (now)

## Slide 7: Data access of HDD
  Access Time = Seek Time + Rotational Delay + Transfer Time

## Slide 8: Redundant Array of Inexpensive Disks (RAID): 1987-1993
Randy Katz and David Patterson: “Use many PC disks to build better storage?”
RAID I built on 1st SPARC, 28 disks
RAID II custom HW, 144 disks
Today, RAID ~$25B industry
RAID students join industry and academia, started own companies (VMware, Panassas)

## Slide 9: The RAID paper
D. A. Patterson, G. Gibson, and R. H. Katz, "A case for redundant arrays of inexpensive disks (RAID)," in SIGMOD'88 Proceedings of the 1988 ACM SIGMOD International Conference on Management of Data, 1988, vol. 17, no. 3, pp. 109-116.
One of the important publications in computer science. http://en.wikipedia.org/wiki/List_of_important_publications_in_computer_science
EMC, HP, IBM, NetApp… have produced so many RAID-related storage products.

## Slide 10: Better Storage?
Capacity?
Performance?
Availability?
……

## Slide 11: RAID Levels
RAID | Min Disks | Storage Efficiency % | Cost | Read Performance | Write Performance
0 | 2 | 100 | Low | Very good | Very good
1 | 2 | 50 | High | Better than a single disk | Slower than a single disk
4 | 3 | (n-1)*100/n | Moderate | Good for reads | Poor for small random writes
5 | 3 | (n-1)*100/n | Moderate | Good for reads | Poor for small random writes
6 | 4 | (n-2)*100/n | Moderate | Good for reads | Poor for small random writes

## Slide 12: 课堂练习（姓名+学号）
假设每个磁盘的容量为10GB，根据RAID技术的相关知识填表：
级别 | 盘个数 | 容量（GB） | 存储效率
RAID0 |  | 60 | 100%
RAID1 | 8 |  | 50%
RAID5 | 8 | 70 | 
RAID6 | 6 |  | 66.7%

## Slide 13: Storage Hierarchy

## Slide 14: Storage Hierarchy

## Slide 15: Intel Optane PM

## Slide 16: New Storage Devices

## Slide 17: New Storage Devices

## Slide 18: Backup

## Slide 19: New Storage Devices

## Slide 20: New Storage Devices

## Slide 21: New Storage Devices

## Slide 22: Performance Comparison